## Slide 1: Mobile Graphics
Patrick Cozzi
University of Pennsylvania
CIS 565 - Fall 2015

## Slide 2: Agenda
Mobile GPUs
Tile-Based Rendering
  Motivation
  Implementation
  Implications on optimizing our code

## Slide 3
Slide by Dave Shreiner

## Slide 4
Slide by Dave Shreiner

## Slide 5: Memory Bandwidth
For 32-bit color, 4 bytes per pixel are needed for display
How many bytes were transferred?

## Slide 6: Memory Bandwidth
For 32-bit color, 4 bytes per pixel are needed for display
How many bytes were transferred?
  12 bytes?
    Read/write depth and stencil
    Write color

## Slide 7: Memory Bandwidth
For 32-bit color, 4 bytes per pixel are needed for display
How many bytes were transferred?
  12 bytes?
    Read/write depth and stencil
    Write color
  What about:
    Textures
    Overdraw
    Blending
    Multisampling
Notes: Over 100 bytes is common.

## Slide 8: Immediate Mode Rendering
Image from http://www.openglinsights.com/
Immediate Mode Rendering (IMR) specifies triangles to be drawn in a current state

## Slide 9: Immediate Mode Rendering
Image from http://www.openglinsights.com/
IMRs can result in overdraw
Notes: Results in unnecessary shading and depth buffer writes

## Slide 10: Immediate Mode Rendering
Image from http://www.openglinsights.com/
Sort front to back to minimize overdraw
Notes: Uses early-z. View-dependent. Needs to be done per frame for dynamic scenes. Translucent objects still need to be rendered back to front.

## Slide 11: Immediate Mode Rendering
Image from http://www.openglinsights.com/
Depth pre-pass to minimize overdraw
Notes: Have to transform vertices twice, but CPU overhead can be low on the second pass. Depth only pass can use double-speed z-only.

## Slide 12: Tile-Based Rendering
Bandwidth uses a significant amount of power consumption
Mobile graphics want to maximum battery life. How?
  Minimize accessing the framebuffer in global memory
Notes: Reducing bandwidth helps power consumption and performance!
Compression helps, but it is not enough.
OpenGL spec says triangles are rendered in order; however, we can reorder and parallelize things under the hood.

## Slide 13: Tile-Based Rendering
Image from http://www.imgtec.com/powervr/insider/docs/PowerVR%20Series5%20Graphics.SGX%20architecture%20guide%20for%20developers.1.0.8.External.pdf
Break framebuffer up into tiles, e.g., 16x16 pixels

## Slide 14: Tile-Based Rendering
Render one tile at a time using all primitives that overlap a tile
Images from http://www.openglinsights.com/

## Slide 15: Tile-Based Rendering
A tile is stored on-chip in the tile buffer
All depth/stencil/color access is on-chip
After the tile is rendered, color is written to global memory
How does this affect vertex processing?
Notes: Sounds like using shared memory in CUDA, right?
Doesn't have to write overdrawn pixels, depth/stencil, etc. to global memory.
Depth/stencil testing and blending are done on chip.

## Slide 16: Tile-Based Rendering
Avoid transforming all vertices in the scene per-tile by storing
  gl_Position and vertex shader varyings
  Fragment shader and uniforms
  Fixed function state, e.g., depth test, etc.
  in a spatial data structure call the frame data (or polygon lists or parameter buffer)
Notes: Frame data is also called polygon lists (ARM) and the parameter buffer (Imagination Technologies).

## Slide 17
Slide by Dave Shreiner

## Slide 18: Tile-Based Rendering
Image from http://www.openglinsights.com/

## Slide 19: What’s the Difference?
Image from http://www.openglinsights.com/
IMR
Tile-Based
Notes: Much less global memory access since a tile is only written to global memory once, and only color is written. However, frame data is now in global memory. As long as there is not too many posted-clipped triangles, the extra global memory access introduced by frame data is much less than the access saved using tiling.

## Slide 20: Framebuffer Clears
glClear is cheap and clears frame data
  Don’t skip it
  Clear everything, e.g., all buffers, no scissor test, etc.
Even better, use EXT_discard_framebuffer:
const GLenum attachments[3] = { COLOR_EXT, DEPTH_EXT, STENCIL_EXT };
glDiscardFramebufferEXT(GL_FRAMEBUFFER, 3, attachments);
Notes: Old school optimizations use to draw the sky box first, etc. to avoid glClear. Don’t do that.

## Slide 21: Tile-Based Deferred Rendering
On PowerVR, only fragments that contribute to the scene are shaded:
Called Tile-Based Deferred Rendering (TBDR)
Image from http://www.imgtec.com/powervr/insider/docs/PowerVR%20Series5%20Graphics.SGX%20architecture%20guide%20for%20developers.1.0.8.External.pdf
Notes: A tile has access to the frame data spatial data structure, and can therefore sort front-to-back unlike IMR.
The image on the right is a view from the left of the camera.
I suspect, in theory, they can do OIT with the frame data too.

## Slide 22: Tile-Based Deferred Rendering
Image from http://www.openglinsights.com/
How does sorting front-to-back and depth prepass affect TBDR?
Notes: No longer useful; wasted CPU time

## Slide 23
Slide by Dave Shreiner
Notes: Video: https://www.youtube.com/watch?v=4pDADEhka_g
Roughly 1.5% overhead from computing and comparing the CRCs.
64-bit CRC. Collisions possible.
More info: http://www.anandtech.com/show/8234/arms-mali-midgard-architecture-explored/7